## Slide 1: Topic: ARDUINO AND IR SENSOR
Tech Toy 2020
1ST ONLINE NATIONAL HACKATHON ON TECHNOLOGICAL INNOVATION FOR TOYS
Created and Presentation by
Tejas M.N
2ND Year student ,B.E in Computer Science
Dr.Ambedkar Institute of Technology,Bangalore
Organized by Start-up Cell:Prakaousol
National Institute of Technology,Arunachal Pradesh
Sposored by TEQUIP-III

## Slide 2: How to control two LED’s using TV remote or any other IR remote using IR sensor and their applications
Objective:
Understand the working principle of IR sensor.

## Slide 3
ARDUINO UNO
The Arduino Uno is an open source microcontrollerboard based on the Microchip ATmega328P microcontroller and developed by Arduino company

## Slide 4
Arduino UNO Board
ATmega328p microcontroller

## Slide 5: Technical specifications of ARDUINO UNO
Microcontroller | ATmega328P
Operating Voltage | 5V
Recommended Input Voltage | 7-12V
Analog Input Pins | 6 (A0 – A5)
Digital I/O Pins | 14 (Out of which 6 provide PWM output)
DC Current on I/O Pins | 40 mA
DC Current on 3.3V Pin | 50 mA
Flash Memory | 32 KB (0.5 KB is used for Bootloader)

## Slide 6
Frequency (Clock Speed) | 16 MHz
Inbuilt LED | Pin 13
Reset button | Resets the microcontroller.
USB Plug | USB-B type to connect to computer
Arduino IDE (Integrated Development Environment) is required to program the Arduino Uno board. Link:https://www.arduino.cc/en/guide/windows
Software required:

## Slide 7: TSOP1738 IR reciever
TSOP1738 is an IR receiver with an amplifier that acts as a switch and converter within a circuit. The basic purpose of TSOP1738 is to convert the IR signal to electric signals. Every IR receiver has a special frequency to operate. TSOP1738 operates on 38KHz IR frequency. In case of higher or lower frequency, it may act due to a current leakage or some other errors but it won’t fully operate. It uses silicon-based technology, which works at the microlevel and very sensitive and efficient to its functions. In summary, TSOP may be smaller in size but its usage with microcontroller and microprocessors makes it smart and secure. TSOP1838 is an improved version of TSOP1738 .

## Slide 8: Working principle of the TSOP1738:
When the IR remote is pressed it sends out IR radiation. The TSOP1738 detects the IR which is switching on and off at the rate of 38Khz. TSOP’s output is active low, means its output will continue to remain HIGH when there is no IR, and becomes low when it detects IR radiation. So as to eliminate interference, the TSOP1738 operates at a particular frequency so that other IRs in the environment can’t interfere, except the modulated IR of particular frequency.

## Slide 9: Components required:
Arduino uno
Breadboard
TSOP1838
IR remote
2 LEDs
Jumpers wires

## Slide 10: Circuit Diagram:
Connect the above mentioned components as shown

## Slide 11: Decoding IR Remote Control Signals using Arduino
When any button of the IR Remote is pressed, the remote sends a code in form of train of encoded pulses using 38Khz modulating frequency. These pulses are received by TSOP1838 sensor and read by Arduino and then Arduino decodes received train of pulse into a hex/bin value and in turn will display it on the serial monitor.

## Slide 12: Requirements:
You need to have the IR remote library https://github.com/z3t0/Arduino-Irremote
Unzip it and place it in your Arduino ‘Libraries’ folder.

## Slide 13: Flowchart:
START
Pin declarations
Receive the ir signal
setup
Initialize output pins and begin serial communication and IR input
A

## Slide 14
If IR signal is detected?
Is result.value
delay(100)
Infinite loop
TRUE
FALSE
Turn off led 1
Turn off led 2
Print “you pressed other button” and result.value
Print “you pressed up arrow button” and result.value
Turn on led 1
Print “you pressed down arrow button” and result.value
Turn on led 2
=584653031?
=584673431?
default
resume
A

## Slide 15: Program:

## Slide 16: Applications:
Home Automation projects
Home security systems
fire detection
proximity sensors
distance measurement
obstacle detection etc…

## Slide 17: Applications in Toys:
Infrared Induction helicopter toys
Infrared remote control toys
UFO flying ball toys for kids
Obstacle avoiding robots etc..

## Slide 18: *****Thank you*****
How to control two LED’s using TV remote or any other IR remote using IR sensor And their Applications
In this presentation we have
Understood the working principle of IR sensor.
Conclusion:

## Slide 19: Approximate cost and time for this project:
Cost : Approximately less than Rs.1000
Time required for making this project: Approximately within one day.